## Slide 1: CSCI 3511 Final Project – Arduino Music Box
Asia Keomanivong

## Slide 2: Music Box

## Slide 3: Functions
  Music sheet (right) is fed through array of infrared LEDs and photodiodes
    Eight columns that can be marked
    Similar to a scantron
  Marks on paper represent note to be played
    Length of mark determines duration of note
  Dark marks impede infrared light so when dark mark passes between an LED and photodiode, the photodiode will have a low reading, indicating that a note should be played
  Each pair of LEDs and photodiodes correspond to the note marked on the sheet
  Sound is played through the passive buzzer

## Slide 4: Materials
  Arduino Mega 2560
    More analog pins
  LM324 Op Amps
  8 IR LEDs
  8 IR photodiodes
  10k potentiometer
  Power supply module
  Perf board
  Passive buzzer
  Jumper wires
  Dupont wires
  10k and 220 ohm resistors
  Solder iron
  A lot of time and patience

## Slide 5: Testing
  First tested the IR LEDs and photodiodes
    Learned how to read photodiodes
    Find out how to impede IR light
      Used black electrical tape
    Used op amps to get better readings from photodiodes
    Used power supply module to get more power
  Soldered components together after array was set
    Used multimeter to ensure good wiring and proper setup
  Wired everything together
    Based off prototyping from IR LED and photodiode array
  Connected passive buzzer with pitches.h to play different tones
  System is fully functional

## Slide 6: Challenges
  Soldering for the first time
  IR photodiodes
    Bad readings
    Op amps
  Power
  Wiring

## Slide 7: Functionality
  Array of IR LEDs and photodiodes
  IR light passes through paper
  If there is a dark mark, IR light does not pass
    Note will play
    Note determined by which photodiode detects mark
  Manual feeding

## Slide 8: Demo

## Slide 9: Final Thoughts
  Enjoyable learning experience
    Learned how to solder
    IR and op amps
  A lot of room for improvements and polish
    Tidy up wiring
    More LEDs and photodiodes for wider range of notes
    Create housing
    Better perf board construction
    Rollers
    Cleaner design overall

## Slide 10: Questions?